Problem 1
Code:
module sixteen_adder();
        reg[15:0] a, b;
        wire[15:0] s;
        wire c_out;

        fulladder FA0(c1, s[0], a[0], b[0], 1'b0);
        fulladder FA1(c2, s[1], a[1], b[1], c1);
        fulladder FA2(c3, s[2], a[2], b[2], c2);
        fulladder FA3(c4, s[3], a[3], b[3], c3);
        fulladder FA4(c5, s[4], a[4], b[4], c4);
        fulladder FA5(c6, s[5], a[5], b[5], c5);
        fulladder FA6(c7, s[6], a[6], b[6], c6);
        fulladder FA7(c8, s[7], a[7], b[7], c7);
        fulladder FA8(c9, s[8], a[8], b[8], c8);
        fulladder FA9(c10, s[9], a[9], b[9], c9);
        fulladder FA10(c11, s[10], a[10], b[10], c10);
        fulladder FA11(c12, s[11], a[11], b[11], c11);
        fulladder FA12(c13, s[12], a[12], b[12], c12);
        fulladder FA13(c14, s[13], a[13], b[13], c13);
        fulladder FA14(c15, s[14], a[14], b[14], c14);
        fulladder FA15(c_out, s[15], a[15], b[15], c15);

        initial begin

        $monitor($time,
        "a=%b, b=%b, s=%b, cout=%b, c1=%b, c2=%b, c3=%b, c4=%b, c5=%b, c6=%b, c7=%b, c8=%b, c9=%b, c10=%b, c11=%b, c12=%b, c13=%b, c14=%b, c15=%b",
        a, b, s, c_out, c1, c2, c3, c4, c5, c6, c7, c8, c9, c10, c11, c12, c13, c14, c15);

        a=-10; b=100;
        #100 $display ("\n", $time, "\n");

        #900 a=63; b=-(-127);
        #100 $display ("\n", $time, "\n");

        #900 a=15; b=95;
        #100 $display ("\n", $time, "\n");

        #900 a=-32; b=79;
        #100 $display ("\n", $time, "\n");

        #900 a=-59; b=-16;
        #100 $display ("\n", $time, "\n");

        #900 a=1000; b=2001;
        #100 $display ("\n", $time, "\n");

        #900 a=-3210; b=15;
        #100 $display ("\n", $time, "\n");

        end

endmodule

module fulladder(cout, si, ai, bi, cin);
        input ai, bi, cin;
        output cout, si;

        xor #1 (si1, ai, bi);
        xor #1 (si, si1, cin);

        and #1 (ci1, ai, bi);
        and #1 (ci2, cin, si1);
        or #1 (cout, ci1, ci2);
endmodule

Inputs:
a=-10; b=100;

a=63; b=-(-127);

a=15; b=95;

a=-32; b=79;

a=-59; b=-16;

a=1000; b=2001;

a=-3210; b=15;

Outputs:
nickelback {~/cse341/a2} > ./a.out
        0a=1111111111110110, b=0000000001100100, s=xxxxxxxxxxxxxxxx, cout=x, c1=x, c2=x, c3=x, c4=x, c5=x, c6=x, c7=x, c8=x, c9=x, c10=x, c11=x, c12=x, c13=x, c14=x, c15=x
        2a=1111111111110110, b=0000000001100100, s=xxxxxxxxxxxxxxx0, cout=x, c1=0, c2=x, c3=1, c4=x, c5=x, c6=1, c7=1, c8=x, c9=x, c10=x, c11=x, c12=x, c13=x, c14=x, c15=x
        3a=1111111111110110, b=0000000001100100, s=xxxxxxxx01xx1x10, cout=x, c1=0, c2=x, c3=1, c4=0, c5=x, c6=1, c7=1, c8=x, c9=x, c10=x, c11=x, c12=x, c13=x, c14=x, c15=x
        4a=1111111111110110, b=0000000001100100, s=xxxxxxxx01x11x10, cout=x, c1=0, c2=0, c3=1, c4=0, c5=x, c6=1, c7=1, c8=1, c9=x, c10=x, c11=x, c12=x, c13=x, c14=x, c15=x
        5a=1111111111110110, b=0000000001100100, s=xxxxxxx001x11010, cout=x, c1=0, c2=0, c3=1, c4=0, c5=0, c6=1, c7=1, c8=1, c9=x, c10=x, c11=x, c12=x, c13=x, c14=x, c15=x
        6a=1111111111110110, b=0000000001100100, s=xxxxxxx001011010, cout=x, c1=0, c2=0, c3=1, c4=0, c5=0, c6=1, c7=1, c8=1, c9=1, c10=x, c11=x, c12=x, c13=x, c14=x, c15=x
        7a=1111111111110110, b=0000000001100100, s=xxxxxx0001011010, cout=x, c1=0, c2=0, c3=1, c4=0, c5=0, c6=1, c7=1, c8=1, c9=1, c10=x, c11=x, c12=x, c13=x, c14=x, c15=x
        8a=1111111111110110, b=0000000001100100, s=xxxxxx0001011010, cout=x, c1=0, c2=0, c3=1, c4=0, c5=0, c6=1, c7=1, c8=1, c9=1, c10=1, c11=x, c12=x, c13=x, c14=x, c15=x
        9a=1111111111110110, b=0000000001100100, s=xxxxx00001011010, cout=x, c1=0, c2=0, c3=1, c4=0, c5=0, c6=1, c7=1, c8=1, c9=1, c10=1, c11=x, c12=x, c13=x, c14=x, c15=x
        10a=1111111111110110, b=0000000001100100, s=xxxxx00001011010, cout=x, c1=0, c2=0, c3=1, c4=0, c5=0, c6=1, c7=1, c8=1, c9=1, c10=1, c11=1, c12=x, c13=x, c14=x, c15=x
        11a=1111111111110110, b=0000000001100100, s=xxxx000001011010, cout=x, c1=0, c2=0, c3=1, c4=0, c5=0, c6=1, c7=1, c8=1, c9=1, c10=1, c11=1, c12=x, c13=x, c14=x, c15=x
        12a=1111111111110110, b=0000000001100100, s=xxxx000001011010, cout=x, c1=0, c2=0, c3=1, c4=0, c5=0, c6=1, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=x, c14=x, c15=x
        13a=1111111111110110, b=0000000001100100, s=xxx0000001011010, cout=x, c1=0, c2=0, c3=1, c4=0, c5=0, c6=1, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=x, c14=x, c15=x
        14a=1111111111110110, b=0000000001100100, s=xxx0000001011010, cout=x, c1=0, c2=0, c3=1, c4=0, c5=0, c6=1, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=x, c15=x
        15a=1111111111110110, b=0000000001100100, s=xx00000001011010, cout=x, c1=0, c2=0, c3=1, c4=0, c5=0, c6=1, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=x, c15=x
        16a=1111111111110110, b=0000000001100100, s=xx00000001011010, cout=x, c1=0, c2=0, c3=1, c4=0, c5=0, c6=1, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=1, c15=x
        17a=1111111111110110, b=0000000001100100, s=x000000001011010, cout=x, c1=0, c2=0, c3=1, c4=0, c5=0, c6=1, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=1, c15=x
        18a=1111111111110110, b=0000000001100100, s=x000000001011010, cout=x, c1=0, c2=0, c3=1, c4=0, c5=0, c6=1, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=1, c15=1
        19a=1111111111110110, b=0000000001100100, s=0000000001011010, cout=x, c1=0, c2=0, c3=1, c4=0, c5=0, c6=1, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=1, c15=1
        20a=1111111111110110, b=0000000001100100, s=0000000001011010, cout=1, c1=0, c2=0, c3=1, c4=0, c5=0, c6=1, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=1, c15=1

        100

        1000a=0000000000111111, b=0000000001111111, s=0000000001011010, cout=1, c1=0, c2=0, c3=1, c4=0, c5=0, c6=1, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=1, c15=1
        1002a=0000000000111111, b=0000000001111111, s=1111111110001000, cout=1, c1=1, c2=1, c3=1, c4=1, c5=1, c6=1, c7=0, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=1, c15=1
        1003a=0000000000111111, b=0000000001111111, s=1111111100111110, cout=0, c1=1, c2=1, c3=1, c4=1, c5=1, c6=1, c7=1, c8=0, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        1004a=0000000000111111, b=0000000001111111, s=0000000010111110, cout=0, c1=1, c2=1, c3=1, c4=1, c5=1, c6=1, c7=1, c8=0, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0

        1100

        2000a=0000000000001111, b=0000000001011111, s=0000000010111110, cout=0, c1=1, c2=1, c3=1, c4=1, c5=1, c6=1, c7=1, c8=0, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        2002a=0000000000001111, b=0000000001011111, s=0000000010101110, cout=0, c1=1, c2=1, c3=1, c4=1, c5=0, c6=0, c7=1, c8=0, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        2003a=0000000000001111, b=0000000001011111, s=0000000011001110, cout=0, c1=1, c2=1, c3=1, c4=1, c5=1, c6=0, c7=1, c8=0, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        2004a=0000000000001111, b=0000000001011111, s=0000000011101110, cout=0, c1=1, c2=1, c3=1, c4=1, c5=1, c6=0, c7=0, c8=0, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        2005a=0000000000001111, b=0000000001011111, s=0000000001101110, cout=0, c1=1, c2=1, c3=1, c4=1, c5=1, c6=0, c7=0, c8=0, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0

        2100

        3000a=1111111111100000, b=0000000001001111, s=0000000001101110, cout=0, c1=1, c2=1, c3=1, c4=1, c5=1, c6=0, c7=0, c8=0, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        3002a=1111111111100000, b=0000000001001111, s=1111111110010001, cout=0, c1=0, c2=0, c3=0, c4=0, c5=1, c6=0, c7=1, c8=0, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        3003a=1111111111100000, b=0000000001001111, s=1111111100001111, cout=0, c1=0, c2=1, c3=1, c4=1, c5=0, c6=1, c7=1, c8=0, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        3004a=1111111111100000, b=0000000001001111, s=1111111101110011, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=1, c7=1, c8=1, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        3005a=1111111111100000, b=0000000001001111, s=1111111001101111, cout=0, c1=0, c2=0, c3=1, c4=1, c5=0, c6=0, c7=1, c8=1, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        3006a=1111111111100000, b=0000000001001111, s=1111111000110111, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        3007a=1111111111100000, b=0000000001001111, s=1111110000101111, cout=0, c1=0, c2=0, c3=0, c4=1, c5=0, c6=0, c7=1, c8=1, c9=1, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        3008a=1111111111100000, b=0000000001001111, s=1111110000111111, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=0, c12=0, c13=0, c14=0, c15=0
        3009a=1111111111100000, b=0000000001001111, s=1111100000101111, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=0, c12=0, c13=0, c14=0, c15=0
        3010a=1111111111100000, b=0000000001001111, s=1111100000101111, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=1, c12=0, c13=0, c14=0, c15=0
        3011a=1111111111100000, b=0000000001001111, s=1111000000101111, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=1, c12=0, c13=0, c14=0, c15=0
        3012a=1111111111100000, b=0000000001001111, s=1111000000101111, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=0, c14=0, c15=0
        3013a=1111111111100000, b=0000000001001111, s=1110000000101111, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=0, c14=0, c15=0
        3014a=1111111111100000, b=0000000001001111, s=1110000000101111, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=0, c15=0
        3015a=1111111111100000, b=0000000001001111, s=1100000000101111, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=0, c15=0
        3016a=1111111111100000, b=0000000001001111, s=1100000000101111, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=1, c15=0
        3017a=1111111111100000, b=0000000001001111, s=1000000000101111, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=1, c15=0
        3018a=1111111111100000, b=0000000001001111, s=1000000000101111, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=1, c15=1
        3019a=1111111111100000, b=0000000001001111, s=0000000000101111, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=1, c15=1
        3020a=1111111111100000, b=0000000001001111, s=0000000000101111, cout=1, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=1, c15=1

        3100

        4000a=1111111111000101, b=1111111111110000, s=0000000000101111, cout=1, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=1, c15=1
        4002a=1111111111000101, b=1111111111110000, s=1111111110110101, cout=1, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=1, c15=1

        4100

        5000a=0000001111101000, b=0000011111010001, s=1111111110110101, cout=1, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=1, c12=1, c13=1, c14=1, c15=1
        5002a=0000001111101000, b=0000011111010001, s=1111101110111001, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=0, c12=0, c13=0, c14=0, c15=0
        5003a=0000001111101000, b=0000011111010001, s=0000001110111001, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=1, c12=0, c13=0, c14=0, c15=0
        5004a=0000001111101000, b=0000011111010001, s=0000101110111001, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=1, c12=0, c13=0, c14=0, c15=0

        5100

        6000a=1111001101110110, b=0000000000001111, s=0000101110111001, cout=0, c1=0, c2=0, c3=0, c4=0, c5=0, c6=0, c7=1, c8=1, c9=1, c10=1, c11=1, c12=0, c13=0, c14=0, c15=0
        6002a=1111001101110110, b=0000000000001111, s=1111110011111001, cout=0, c1=0, c2=1, c3=1, c4=0, c5=0, c6=0, c7=0, c8=0, c9=0, c10=0, c11=1, c12=0, c13=0, c14=0, c15=0
        6003a=1111001101110110, b=0000000000001111, s=1111101101110101, cout=0, c1=0, c2=1, c3=1, c4=0, c5=0, c6=0, c7=0, c8=0, c9=1, c10=1, c11=0, c12=0, c13=0, c14=0, c15=0
        6004a=1111001101110110, b=0000000000001111, s=1111010101110101, cout=0, c1=0, c2=1, c3=1, c4=1, c5=0, c6=0, c7=0, c8=0, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        6005a=1111001101110110, b=0000000000001111, s=1111001101100101, cout=0, c1=0, c2=1, c3=1, c4=1, c5=0, c6=0, c7=0, c8=0, c9=0, c10=1, c11=0, c12=0, c13=0, c14=0, c15=0
        6006a=1111001101110110, b=0000000000001111, s=1111011101100101, cout=0, c1=0, c2=1, c3=1, c4=1, c5=1, c6=0, c7=0, c8=0, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        6007a=1111001101110110, b=0000000000001111, s=1111001101000101, cout=0, c1=0, c2=1, c3=1, c4=1, c5=1, c6=0, c7=0, c8=0, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        6008a=1111001101110110, b=0000000000001111, s=1111001101000101, cout=0, c1=0, c2=1, c3=1, c4=1, c5=1, c6=1, c7=0, c8=0, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        6009a=1111001101110110, b=0000000000001111, s=1111001100000101, cout=0, c1=0, c2=1, c3=1, c4=1, c5=1, c6=1, c7=0, c8=0, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        6010a=1111001101110110, b=0000000000001111, s=1111001100000101, cout=0, c1=0, c2=1, c3=1, c4=1, c5=1, c6=1, c7=1, c8=0, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0
        6011a=1111001101110110, b=0000000000001111, s=1111001110000101, cout=0, c1=0, c2=1, c3=1, c4=1, c5=1, c6=1, c7=1, c8=0, c9=0, c10=0, c11=0, c12=0, c13=0, c14=0, c15=0

        6100

Comments:
The 16-bit ripple carry adder works by simply extending the 1-bit full adder sixteen times, successively passing in the carry outs of the addition of the previous bit.
Problem 2

Code:
module four_comparator();
        reg[3:0] a, b;
        wire[2:0] g;

        not #1 (not_b3, b[3]);
        and #1 (and3, not_b3, a[3]);

        xnor #1 (xnor3, b[3], a[3]);

        not #1 (not_b2, b[2]);
        and #1 (and2, xnor3, not_b2, a[2]);

        xnor #1 (xnor2, a[2], b[2]);

        not #1 (not_b1, b[1]);
        and #1 (and1, xnor3, xnor2, not_b1, a[1]);

        xnor #1 (xnor1, a[1], b[1]);

        not #1 (not_b0, b[0]);
        and #1 (and0, xnor3, xnor2, xnor1, not_b0, a[0]);

        xnor #1 (xnor0, a[0], b[0]);

        or #1 (g[0], and3, and2, and1, and0);

        and #1 (g[1], xnor3, xnor2, xnor1, xnor0);

        nor(g[2], g[1], g[0]);

        initial begin

        $monitor($time,
        "a=%b, b=%b, a > b --> %b, a = b --> %b, a < b --> %b",
        a, b, g[0], g[1], g[2]);

        a=2; b=4;
        #100 $display ("\n", $time, "\n");

        #900 a=4; b=10;
        #100 $display ("\n", $time, "\n");

        #900 a=0; b=0;
        #100 $display ("\n", $time, "\n");

        #900 a=7; b=5;
        #100 $display ("\n", $time, "\n");

        #900 a=14; b=15;
        #100 $display ("\n", $time, "\n");

        #900 a=12; b=3;
        #100 $display ("\n", $time, "\n");

        #900 a=15; b=15;
        #100 $display ("\n", $time, "\n");

        end

endmodule

Inputs:
a=2; b=4;

a=4; b=10;

a=0; b=0;

a=7; b=5;

a=14; b=15;

a=12; b=3;

a=15; b=15;

Outputs:
nickelback {~/cse341/a2} > ./a.out
        0a=0010, b=0100, a > b --> z, a = b --> z, a < b --> x
        1a=0010, b=0100, a > b --> x, a = b --> z, a < b --> x
        2a=0010, b=0100, a > b --> x, a = b --> 0, a < b --> x
        3a=0010, b=0100, a > b --> 0, a = b --> 0, a < b --> 1

        100

        1000a=0100, b=1010, a > b --> 0, a = b --> 0, a < b --> 1

        1100

        2000a=0000, b=0000, a > b --> 0, a = b --> 0, a < b --> 1
        2002a=0000, b=0000, a > b --> 0, a = b --> 1, a < b --> 0

        2100

        3000a=0111, b=0101, a > b --> 0, a = b --> 1, a < b --> 0
        3002a=0111, b=0101, a > b --> 1, a = b --> 0, a < b --> 0

        3100

        4000a=1110, b=1111, a > b --> 1, a = b --> 0, a < b --> 0
        4003a=1110, b=1111, a > b --> 0, a = b --> 0, a < b --> 1

        4100

        5000a=1100, b=0011, a > b --> 0, a = b --> 0, a < b --> 1
        5003a=1100, b=0011, a > b --> 1, a = b --> 0, a < b --> 0

        5100

        6000a=1111, b=1111, a > b --> 1, a = b --> 0, a < b --> 0
        6002a=1111, b=1111, a > b --> 1, a = b --> 1, a < b --> 0
        6003a=1111, b=1111, a > b --> 0, a = b --> 1, a < b --> 0

        6100

Comments:
This implementation of the 4-bit comparator compares any two numbers (which values are between 0 and 15) as a 4-bit unsigned binary representation.
Problem 3

Code:
module sixteen_cla();
        reg[15:0] a, b;
        wire[3:0] cout, p, g;
        wire[15:0] s;

        four_cla F0(cout[0], s[3:0], p[0], g[0], a[3:0], b[3:0], 1'b0);
        and #1 (t0, 1'b0, p[0]);
        or #1 (c1, g[0], t0);

        four_cla F1(cout[1], s[7:4], p[1], g[1], a[7:4], b[7:4], c1);
        and #1 (t1, g[0], p[1]);
        and #1 (t2, 1'b0, p[0], p[1]);
        or #1 (c2, g[1], t1, t2);

        four_cla F2(cout[2], s[11:8], p[2], g[2], a[11:8], b[11:8], c2);
        and #1 (t3, g[1], p[2]);
        and #1 (t4, g[0], p[1], p[2]);
        and #1 (t5, 1'b0, p[0], p[1], p[2]);
        or #1 (c3, g[2], t3, t4, t5);

        four_cla F3(cout[3], s[15:12], p[3], g[3], a[15:12], b[15:12], c3);
        and #1 (t6, g[2], p[3]);
        and #1 (t7, g[1], p[2], p[3]);
        and #1 (t8, g[0], p[1], p[2], p[3]);
        and #1 (t9, 1'b0, p[0], p[1], p[2], p[3]);
        or #1 (c4, g[3], t6, t7, t8, t9);

        initial begin

        $monitor($time,
        "a=%b, b=%b, s=%b",
        a, b, s);

        a=-10; b=100;
        #100 $display ("\n", $time, "\n");

        #900 a=63; b=-(-127);
        #100 $display ("\n", $time, "\n");

        #900 a=15; b=95;
        #100 $display ("\n", $time, "\n");

        #900 a=-32; b=79;
        #100 $display ("\n", $time, "\n");

        #900 a=-59; b=-16;
        #100 $display ("\n", $time, "\n");

        #900 a=1000; b=2001;
        #100 $display ("\n", $time, "\n");

        #900 a=-3210; b=15;
        #100 $display ("\n", $time, "\n");

        end

endmodule

module four_cla(cout, s, pi, gi, a, b, cin);
        input cin;
        input[3:0] a, b;
        output cout, pi, gi;
        output[3:0] s;

        xor #1 (p0, a[0], b[0]);
        and #1 (g0, a[0], b[0]);

        xor #1 (p1, a[1], b[1]);
        and #1 (g1, a[1], b[1]);

        xor #1 (p2, a[2], b[2]);
        and #1 (g2, a[2], b[2]);

        xor #1 (p3, a[3], b[3]);
        and #1 (g3, a[3], b[3]);

        and #1 (and0, p0, cin);
        or #1 (c1, g0, and0);

        and #1 (and1, p1, g0);
        and #1 (and2, p1, p0, cin);
        or #1 (c2, g1, and2, and1);

        and #1 (and3, p2, g1);
        and #1 (and4, p2, p1, g0);
        and #1 (and5, p2, p1, p0, cin);
        or #1 (c3, g2, and5, and4, and3);

        and #1 (and6, p3, g2);
        and #1 (and7, p3, p2, g1);
        and #1 (and8, p3, p2, p1, g0);
        and #1 (and9, p3, p2, p1, p0, cin);
        or #1 (cout, g3, and9, and8, and7, and6);

        xor #1 (s[0], p0, cin);
        xor #1 (s[1], p1, c1);
        xor #1 (s[2], p2, c2);
        xor #1 (s[3], p3, c3);

        and #1 (pi, p3, p2, p1, p0);
        and #1 (t0, g0, p1, p2, p3);
        and #1 (t1, g1, p2, p3);
        and #1 (t2, g2, p3);
        or #1 (gi, g3, t2, t1, t0);

endmodule

Inputs:
a=-10; b=100;

a=63; b=-(-127);

a=15; b=95;

a=-32; b=79;

a=-59; b=-16;

a=1000; b=2001;

a=-3210; b=15;

Outputs:
nickelback {~/cse341/a2} > ./a.out
        0a=1111111111110110, b=0000000001100100, s=xxxxxxxxxxxxxxxx
        2a=1111111111110110, b=0000000001100100, s=xxxxxxxxxxxxxxx0
        3a=1111111111110110, b=0000000001100100, s=xxxxxxxx01xx1x10
        4a=1111111111110110, b=0000000001100100, s=xxxxxxxx01xx1010
        5a=1111111111110110, b=0000000001100100, s=xxxxxxx001x11010
        6a=1111111111110110, b=0000000001100100, s=xxx0xxx001x11010
        7a=1111111111110110, b=0000000001100100, s=xxx0000001011010
        8a=1111111111110110, b=0000000001100100, s=0000000001011010

        100

        1000a=0000000000111111, b=0000000001111111, s=0000000001011010
        1002a=0000000000111111, b=0000000001111111, s=1111111110001000
        1003a=0000000000111111, b=0000000001111111, s=1111111100101110
        1004a=0000000000111111, b=0000000001111111, s=0001000110111110
        1005a=0000000000111111, b=0000000001111111, s=0000000010111110

        1100

        2000a=0000000000001111, b=0000000001011111, s=0000000010111110
        2002a=0000000000001111, b=0000000001011111, s=0000000010101110
        2003a=0000000000001111, b=0000000001011111, s=0000000011001110
        2004a=0000000000001111, b=0000000001011111, s=0000000001101110

        2100

        3000a=1111111111100000, b=0000000001001111, s=0000000001101110
        3002a=1111111111100000, b=0000000001001111, s=1111111110010001
        3003a=1111111111100000, b=0000000001001111, s=1111111100011111
        3004a=1111111111100000, b=0000000001001111, s=1111111100101111
        3005a=1111111111100000, b=0000000001001111, s=1111111000101111
        3006a=1111111111100000, b=0000000001001111, s=1110111000101111
        3007a=1111111111100000, b=0000000001001111, s=1110000000101111
        3008a=1111111111100000, b=0000000001001111, s=0000000000101111

        3100

        4000a=1111111111000101, b=1111111111110000, s=0000000000101111
        4002a=1111111111000101, b=1111111111110000, s=1111111110110101

        4100

        5000a=0000001111101000, b=0000011111010001, s=1111111110110101
        5002a=0000001111101000, b=0000011111010001, s=1111101110111001
        5003a=0000001111101000, b=0000011111010001, s=0001001110111001
        5004a=0000001111101000, b=0000011111010001, s=0000101110111001

        5100

        6000a=1111001101110110, b=0000000000001111, s=0000101110111001
        6002a=1111001101110110, b=0000000000001111, s=1111110011111001
        6003a=1111001101110110, b=0000000000001111, s=1111101001110101
        6004a=1111001101110110, b=0000000000001111, s=1111010101110101
        6005a=1111001101110110, b=0000000000001111, s=1111010101100101
        6006a=1111001101110110, b=0000000000001111, s=1111001101100101
        6007a=1111001101110110, b=0000000000001111, s=1111001110000101

        6100

Comments:
Uses the implementation seen in Appendix C of the textbook.
CSE341 Computer Organization, Spring 2011
Lab #2

By:
Alexander Simeonov
Sheldon Ooi
Yi Man Chia